## Slide 1: Design of Digital Circuits Lecture 22a: Memory Organization and Memory Technology
Prof. Onur Mutlu
ETH Zurich
Spring 2019
16 May 2019

## Slide 2: Readings for This Lecture and Next
Memory Hierarchy and Caches
Required
  H&H Chapters 8.1-8.3
  Refresh: P&P Chapter 3.5
Recommended
  An early cache paper by Maurice Wilkes
    Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.

## Slide 3: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 4: What is A Computer?
We will cover all three components
Memory
(program
and data)
I/O
Processing
control
(sequencing)
datapath

## Slide 5: Memory (Programmer’s View)

## Slide 6: Abstraction: Virtual vs. Physical Memory
Programmer sees virtual memory
  Can assume the memory is “infinite”
Reality: Physical memory size is much smaller than what the programmer assumes
The system (system software + hardware, cooperatively) maps virtual memory addresses to physical memory
  The system automatically manages the physical memory space transparently to the programmer
+ Programmer does not need to know the physical size of memory nor manage it  A small physical memory can appear as a huge one to the programmer  Life is easier for the programmer
-- More complex system software and architecture
A classic example of the programmer/(micro)architect tradeoff

## Slide 7: (Physical) Memory System
You need a larger level of storage to manage a small amount of physical memory automatically
   Physical memory has a backing store: disk
We will first start with the physical memory system
For now, ignore the virtualphysical indirection
We will get back to it later, if time permits…

## Slide 8: Idealism
Instruction
Supply
Pipeline
(Instruction
execution)
Data
Supply
- Zero latency access
- Infinite capacity
- Zero cost
- Perfect control flow
No pipeline stalls
Perfect data flow
(reg/memory dependencies)
Zero-cycle interconnect
(operand communication)
Enough functional units
Zero latency compute
Zero latency access
Infinite capacity
- Infinite bandwidth
Zero cost

## Slide 9: Quick Overview of Memory Arrays

## Slide 10: How Can We Store Data?
Flip-Flops (or Latches)
  Very fast, parallel access
  Very expensive (one bit costs tens of transistors)
Static RAM (we will describe them in a moment)
  Relatively fast, only one data word at a time
  Expensive (one bit costs 6 transistors)
Dynamic RAM (we will describe them a bit later)
  Slower, one data word at a time, reading destroys content (refresh), needs special process for manufacturing
  Cheap (one bit costs only one transistor plus one capacitor)
Other storage technology (flash memory, hard disk, tape)
  Much slower, access takes a long time, non-volatile
  Very cheap (no transistors directly involved)

## Slide 11: Array Organization of Memories
Goal: Efficiently store large amounts of data
  A memory array (stores data)
  Address selection logic (selects one row of the array)
  Readout circuitry (reads data out)
An M-bit value can be read or written at each unique N-bit address
  All values can be accessed, but only M-bits at a time
  Access restriction allows more compact organization

## Slide 12: Memory Arrays
Two-dimensional array of bit cells
  Each bit cell stores one bit
An array with N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (number of words)
  Width: number of columns (size of word)
  Array size: depth × width = 2N × M

## Slide 13: Memory Array Example
22 × 3-bit array
Number of words: 4
Word size: 3-bits
For example, the 3-bit word stored at address 10 is 100

## Slide 14: Larger and Wider Memory Array Example

## Slide 15: Memory Array Organization (I)
Storage nodes in one column connected to one bitline
Address decoder activates only ONE wordline
Content of one line of storage available at output

## Slide 16: Memory Array Organization (II)
Storage nodes in one column connected to one bitline
Address decoder activates only ONE wordline
Content of one line of storage available at output
10
1
0
0
Active wordline

## Slide 17: How is Access Controlled?
Access transistors configured as switches connect the bit storage to the bitline.
Access controlled by the wordline
DRAM
SRAM

## Slide 18: Building Larger Memories
Requires larger memory arrays
Large  slow
How do we make the memory large without making it very slow?
Idea: Divide the memory into smaller arrays and interconnect the arrays to input/output buses
  Large memories are hierarchical array structures
  DRAM: Channel  Rank  Bank  Subarrays  Mats

## Slide 19: General Principle: Interleaving (Banking)
Interleaving (banking)
  Problem: a single monolithic large memory array takes long to access and does not enable multiple accesses in parallel
  Goal: Reduce the latency of memory array access and enable multiple accesses in parallel
  Idea: Divide a large array into multiple banks that can be accessed independently (in the same cycle or in consecutive cycles)
    Each bank is smaller than the entire memory storage
    Accesses to different banks can be overlapped
  A Key Issue: How do you map data to different banks? (i.e., how do you interleave data across banks?)

## Slide 20: Memory Technology: DRAM and SRAM

## Slide 21: Memory Technology: DRAM
Dynamic random access memory
Capacitor charge state indicates stored value
  Whether the capacitor is charged or discharged indicates storage of 1 or 0
  1 capacitor
  1 access transistor
Capacitor leaks through the RC path
  DRAM cell loses charge over time
  DRAM cell needs to be refreshed
row enable
_bitline

## Slide 22: Memory Technology: SRAM
Static random access memory
Two cross coupled inverters store a single bit
  Feedback path enables the stored value to persist in the “cell”
  4 transistors for storage
  2 transistors for access
row select
bitline
_bitline

## Slide 23: Memory Bank Organization and Operation
Read access sequence:
1. Decode row address & drive word-lines
2. Selected bits drive bit-lines
• Entire row read
3. Amplify row data
4. Decode column address & select subset of row
• Send to output
5. Precharge bit-lines
• For next access

## Slide 24: SRAM (Static Random Access Memory)
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m diff pairs
2n
n
m
1
row select
bitline
_bitline
n+m
Read Sequence
  1. address decode
  2. drive row select
  3. selected bit-cells drive bitlines
  (entire row is read together)
  4. differential sensing and column select
  (data is ready)
  5. precharge all bitlines
  (for next read or write)
Access latency dominated by steps 2 and 3
Cycling time dominated by steps 2, 3 and 5
  step 2 proportional to 2m
  step 3 and 5 proportional to 2n

## Slide 25: DRAM (Dynamic Random Access Memory)
row enable
_bitline
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m
2n
n
m
1
RAS
CAS
A DRAM die comprises
of multiple such arrays
Bits stored as charges on node capacitance (non-restorative)
  bit cell loses charge when read
  bit cell loses charge over time
Read Sequence
  1~3 same as SRAM
  4. a “flip-flopping” sense amp amplifies and regenerates the bitline, data bit is mux’ed out
  5. precharge all bitlines
Destructive reads
Charge loss over time
Refresh: A DRAM controller must periodically read each row within the allowed refresh time (10s of ms) such that charge is restored

## Slide 26: DRAM vs. SRAM
DRAM
  Slower access (capacitor)
  Higher density (1T 1C cell)
  Lower cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
SRAM
  Faster access (no capacitor)
  Lower density (6T cell)
  Higher cost
  No need for refresh
  Manufacturing compatible with logic process (no capacitor)

## Slide 27: Design of Digital Circuits Lecture 22a: Memory Organization and Memory Technology
Prof. Onur Mutlu
ETH Zurich
Spring 2019
16 May 2019